## Slide 1: 61.5 m blade layup
Intended uses for blade model
  A starting point for blade design optimization or parameter studies
  Blade structural design tool verifications and validations
IEC Turbine Class I-B (same as NREL 5 MW)
120 m rotor size (same as NREL 5 MW)
Not intended uses for blade model
  Not a model for effective CFD simulation; Ray Chow’s 5 MW blade model is more appropriate
  Not an optimal blade design; an optimized blade was created and documented in SAND2014-3136, Effects of Increasing Tip Velocity on Wind Turbine Rotor Design
Blade geometry
  Replicated the chord, twist, and thickness schedule of the NREL 5 MW reference
  Used the same airfoils as the NREL 5 MW reference

## Slide 2: 61.5 m blade layup
IEC DLC | Desc.
DLC 1.2 | NTM
DLC 1.3 | ETM
DLC 1.4 | ECD
DLC 1.5 | EWS
DLC 6.1 | EWM50
DLC 6.2 | EEWM01
Design load cases used
Materials
  Materials properties were the same as the Sandia 100 m blade model; blade construction is glass fiber with carbon fiber spar caps
Blade layup design requirements
  Meet or exceed a subset of basic IEC design criteria
  Matched overall mass of NREL 5MW blade—17,740 kg
  Safety factors for material strengths and loads were defined using a simple approach that is based on IEC
  IECWind was used to generate load cases
  Panel buckling, composite fatigue, and maximum blade tip deflection were used to drive the layup design